## Slide 1
DIGITAL LOGIC DESIGN · KLH UNIVERSITY
Smart Parking System
Combinational Logic Implementation
Logic League

## Slide 2
Circuit Simulation in Logisim
This slide presents the Logisim-based implementation of the smart parking circuit, showing how combinational logic gates work together to detect parking availability and control vehicle entry.
Parking Entry Logic
Input pin A
Sensor A state
NOT Gate
Inverts FULL to AVAILABLE
Input pin D
Sensor D state
Input pin C
Sensor C state
Input pin B
Sensor B state
4‑Input AND Gate
Outputs FULL when all high
The diagram above illustrates the signal flow from sensor inputs through the AND and NOT gates to the final entry gate control output.

## Slide 3
Components Used
4 Input Pins
Represent parking slot sensors A, B, C, and D
4-Input AND Gate
Outputs HIGH only when all four slots are occupied
NOT Gate
Inverts the FULL signal to produce AVAILABLE output
Output Pins / LEDs
Visual indicators for FULL and AVAILABLE status
Connecting wires link all components, enabling signal flow from inputs through logic gates to outputs.

## Slide 4
Logic Implementation
Boolean Expressions
FULL = A · B · C · D
Output is HIGH only when all four parking slots are occupied simultaneously.
AVAILABLE = ¬(A · B · C · D)
Inverted FULL signal — HIGH when at least one slot is free.
Truth Table (A, B, C, D → FULL / AVAILABLE)
A
B
C
D
FULL
AVAILABLE
0
0
0
0
0
1
0
1
1
0
0
1
1
1
1
0
0
1
1
1
1
1
1
0

## Slide 5
Testing in Logisim
Verify Results
Run Simulation
Set Inputs
Logisim's interactive environment allows real-time toggling of input pins, making it easy to validate all 16 input combinations and confirm correct gate behavior before hardware deployment.

## Slide 6
SLIDE 9
Benefits & Applications
The smart parking system delivers practical advantages for drivers and facility operators, with broad applicability across urban and institutional environments.

## Slide 7
Key Advantages
Saves Time
Drivers know availability before entering, eliminating search time
Reduces Fuel Waste
Fewer circling loops means lower fuel consumption per visit
Eases Congestion
Controlled entry prevents bottlenecks at parking entrances
Low Cost
Simple gate logic requires minimal hardware investment
Scalable Design
Easily expanded to monitor additional parking slots

## Slide 8
Real-World Applications
Shopping Malls
High-traffic retail environments with multi-level parking
Colleges & Universities
Student and faculty parking management across campuses
Hospitals
Critical access for patients, visitors, and emergency vehicles
Railway Stations
Long-term commuter parking with high daily turnover
Airports
Multi-zone parking with real-time availability displays
Smart Cities
IoT-integrated urban infrastructure and traffic management

## Slide 9
SLIDE 10
Conclusion
This project demonstrates how combinational logic can solve a real-world parking problem — detecting slot availability, identifying when the lot is full, and controlling vehicle entry with minimal hardware.
Detects Availability
Monitors all four parking slots in real time
Identifies FULL State
AND gate triggers when all slots are occupied
Controls Entry
NOT gate allows entry only when space is available
Foundation for IoT
Scalable architecture ready for smart city integration

## Slide 10
Thank You
Team: Logic League
Mathi Dhanvanth
Allam Akshaya
Chidura Adhitya
Kunku Abhinaya
KLH University
Project Summary
A 4-input combinational logic circuit using an AND gate and NOT gate to manage smart parking entry — simulated and validated in Logisim.
DIGITAL LOGIC DESIGN
KLH UNIVERSITY